MIC-3389 Dual/Single CPU, Heat Sink and Fan

Installation Guide

The MIC-3389 accepts dual or single Intel Socket 370 Pentium III processor. For the dual CPU operation on the MIC-3389, the two CPUs have to be the same type (PC133 -compliant) and the same speed (up to 1 GHz). In order to meet critical environmental conditions and the physical space of the MIC-3389 at the same time, Advantech designed a heat sink together with two slim fans to fulfill both needs.

The manual and drivers for MIC-3389 are included in the CD.

Single CPU Installation:

Dual CPU Installation:

Note: There are two power modules designed for the MIC-3389 board. For the dual CPU operation on the MIC-3389, it has to install the both power modules onto the MIC-3389.

Note: For the single CPU operation on the MIC-3389, it has to install one CPU terminator into the rest CPU socket and do not install the power module beside the CPU terminator.

Note: To have better ventilation, we still suggest users to install the both slim fans, even if there is only one CPU installed on the MIC-3389 board.

P/N : 2002338910